## Slide 1
INTERNET
TECHNOLOGIES
MULTI-AS INTERNET ARCHITECTURE WITH
BGP, OSPF, VLANS, SERVICES AND SECURITY
Student: Ișfan Ștefan
Programme of study: Physics applied in smart technologies and communications (Master - Second Year)
"Alexandru Ioan Cuza" University of Iaşi - Faculty of Physics
Academic Year: 2025-2026

## Slide 2
WHY DOES THIS
NETWORK EXIST?
  CIA Triad: Confidentiality, integrity, availability
  Need to protect IT resources and services
  Need for redundancy and advanced routing policies
  CIA Visual: CIA diagram (triangle or simple table)
INTERNET
TECHNOLOGIES

## Slide 3
COMPLETE
TOPOLOGY
INTERNET
TECHNOLOGIES

## Slide 4
IP ADDRESSING
  Networking for maximum efficiency
  Clear separation of broadcast domains
  Ground rules for private IP addresses
  Unique gateways on each segment
Segment | Network | Gateway | Usage
ISP ↔ CompA | 10.0.1.0/30 | 10.0.1.1 (ISP) 10.0.1.2 (Border) | eBGP Link
ISP ↔ CompB | 10.0.2.0/30 | 10.0.2.1 (ISP) 10.0.2.2 (Border) | eBGP Link
CompA Border ↔ Core | 192.168.100.0/30 | 192.168.100.1 (Border) 192.168.100.2 (Core) | iBGP/OSPF Link
VLAN 10 (Admin) | 192.168.10.0/24 | 192.168.10.1 | Privileged users
VLAN 20 (Servers) | 192.168.20.0/24 | 192.168.20.1 | DNS, Web, DHCP
VLAN 30 (Users) | 192.168.30.0/24 | 192.168.30.1 | Regular users
CompB LAN | 172.16.1.0/24 | 172.16.1.1 | Simple internal network
INTERNET
TECHNOLOGIES

## Slide 5
EBGP - INTERNET PROTOCOL
INTERNET
TECHNOLOGIES

## Slide 6
OSPF
  State: FULL → full synchronization
  Routes to ISP are in OSPF
  Metrics show logical topology
  The basis for future redundancy
INTERNET
TECHNOLOGIES

## Slide 7
VLAN
Switch Configuration (CompA-SW1)
Connection to Router
  Broadcast isolation security
  Different access policies per VLAN
  Flexibility in reorganization
  Broadcast domain reduction
  Isolation security
  Flexible management
  Granular access policies
INTERNET
TECHNOLOGIES

## Slide 8
ROUTER-ON-A-STICK
  1 physical port → 3 logical interfaces
  Each VLAN has its own gateway
  DHCP for relay between VLANs
  All interfaces are UP/UP (functional)
INTERNET
TECHNOLOGIES

## Slide 9
DNS
1. Configuration
2. Testing
3. Real application
INTERNET
TECHNOLOGIES

## Slide 10
WEB SERVER
INTERNET
TECHNOLOGIES

## Slide 11
DHCP
INTERNET
TECHNOLOGIES

## Slide 12
TESTING (CONNECTIVITY)
Ping: 0% packet loss
Traceroute: 5 hops through 3 ASs
PC-Admin → VLAN 10 → CompA-Core → CompA-Border → ISP → CompB-Border → PC-CompB1
INTERNET
TECHNOLOGIES

## Slide 13
SIMULATION MODE
INTERNET
TECHNOLOGIES

## Slide 14
SECURITY
  VLAN Isolation (Layer 2): ​​Physical separation of broadcast domains
  ACL Filtering (Layer 3): Granular IP-based control
  Defense in Depth: Multiple layers of security
INTERNET
TECHNOLOGIES
Strat | Tehnology | Protection
Layer 2 | VLAN | Department isolation
Layer 3 | ACL | Traffic filtering
Layer 4 | (Future) Firewall | Stateful inspection

## Slide 15
CONCLUSIONS
  Multi-AS architecture with BGP for routing between autonomous systems
  OSPF for fast and scalable internal routing
  Network segmentation via VLANs and router-on-a-stick
  Integrated services: DNS, HTTP, DHCP
  Full validated connectivity between all nodes
Achievements:
Perspectives:
  Future extensions: firewall, BGP redundancy, IPv6
  Solid foundation for real enterprise deployments
INTERNET
TECHNOLOGIES

## Slide 16
THANK YOU!
INTERNET
TECHNOLOGIES